## Slide 1
Dali, Salvador. The Persistence of Memory. 1931.
Museum of Modern Art. New York City.
Remote Memory Persistency
Aasheesh Kolli
Jayneel Gandhi
Irina Calciu
Stanko Novakovic

## Slide 2: Why persistence?
2
Data must always be recoverable, even in the
presence of unexpected failures (not uncommon)

## Slide 3: Conventional recovery solutions
3
Non-volatile, block storage device
Slow,

## Slide 4: Persistent Memory (PM)
Non-volatility
Performance
Can revolutionize recovery data management

## Slide 5: Persistent Memory (PM)
Intel and Micron’s PM offering
(Expected in 2019*)
Can revolutionize recovery data management

## Slide 6: Future persistent memory systems
Store inst.
CPU
Volatile
Memory
Persistent
Memory
Recovery
Store inst.
Recoverable data
Promise: In-memory, recoverable data

## Slide 7: Recovery needs ordered PM updates
Recoverable
In-memory data
fillNewNode()
updateTailPtr()
Task: Fill node and add to linked list, safely

## Slide 8: Recovery needs ordered PM updates
In-memory data
Task: Fill node and add to linked list, safely
fillNewNode()
updateTailPtr()
Recoverable
No ordering  No recovery

## Slide 9: Hidden sources of reordering
fillNewNode()
updateTailPtr()
St A = x
St B = y
St A ≤ St B, for recovery
Core
Caches
St A = x
St B = y
A
B
Recovery violated!
Sources of reordering
Compiler
Cores
Caches
Memory Controller
Need primitives to express order of PM writes

## Slide 10: Memory persistency models
Programmers can express write order to PM
Hardware enforces write order
Example: x86’s clflush/clflushopt/clwb insts
Only helps persist data to local memory
[Condit ‘09] [Pelley ‘14] [Intel ‘14] [Kolli ‘15] [Joshi ‘15] [ARM ‘16]
Need remote memory persistency models
Fault tolerance, memory disaggregation, etc.

## Slide 11: Challenges - I
Core-1
Core-2
L1 $
L1 $
LLC
PM
Network
Core-1
Core-2
L1 $
L1 $
LLC
PM
Remote
NIC
Local
NIC
New hidden sources of buffering/reordering
Local system
Remote system

## Slide 12: Challenges - II
Manage increased memory latencies
  <50ns vs ~2us
Use network bandwidth efficiently
  Load/Store interface not optimal over the network
Extend local memory persistency models
Need HW-SW co-design to address challenges

## Slide 13: Thank you!

## Slide 14
Dali, Salvador. The Persistence of Memory. 1931.
Museum of Modern Art. New York City.
Remote Memory Persistency
Aasheesh Kolli
Jayneel Gandhi
Irina Calciu
Stanko Novakovic